## Slide 1: From Grass to Gas: An Inquiry Based Study of Enzyme
Bio-Rad Biotechnology Explorer™ Biofuel Enzyme Kit

## Slide 2: Instructors - Bio-Rad Curriculum and Training Specialists
Sherri Andrews, Ph.D., Eastern US
sherri_andrews@bio-rad.com
Damon Tighe, Western US
damon_tighe@bio-rad.com
Leigh Brown, M.A., Central US
leigh_brown@bio-rad.com

## Slide 3: What are enzymes? Molecules, usually proteins, that speed up the rate of a reaction by decreasing the activation energy required without themselves being altered or used up
Enzyme Class | Example
Oxidoreductase (transfer of electrons) | Firefly Luciferase – oxidizes luciferin to produce oxyluciferin and light
Transferase (group-transfer reactions) | Hexokinase – transfers a phosphate group to glucose to make glucose-6-phosphate
Hydrolase (hydrolysis reactions) | Cellobiase – breaks down cellobiose
Lyase (double bond reactions) | Histidine decarboxylase – generates histimine from histidine
Isomerase (transfers to create a new isomers) | Glucose-6-Phosphate isomerase – converts G-6-P to fructose-6-phosphate
Ligase (forms covalent bonds) | DNA Ligase – covalently bonds two pieces of DNA
Background - Enzymes

## Slide 4: How do enzymes work?
Substrate (S) Product (P)
ENERGY
REACTION COORDINATE
S
P
S*
Eact
S*enz
Eact
Enzyme
Background - Enzymes

## Slide 5: How do enzymes work?
Substrate free in solution
Substrate binds to a specific cleft or groove in the enzyme
Activation energy barrier is overcome and reaction occurs
Product is released and enzyme is free to catalyze another reaction
Background - Enzymes

## Slide 6: What are biofuels?
Biodiesel
Ethanol from starches/sugars
Cellulosic ethanol
Butanol
Fuels that are produced from a biological source
Oil – biofuel, but very long production cycle (millions of years)
Short cycle Biofuels
Background - Biofuels

## Slide 7: Cellulosic ethanol production
A
B
C
D
Background - Biofuels

## Slide 8: Cellulose breakdown
Cellobiase
Exocellulases
Endocellulases
Glucose
1. Heat, acid, ammonia or other treatment
2. Enzyme mixture added
Background – Biofuels production

## Slide 9: Cellobiose breakdown- a closer look
+
Cellobiose + H2O 2 Glucose
4
1
5
6
4
2
3
1
Background - cellobiose

## Slide 10: Protocol Highlights: Using a colorimetric substrate to track reaction rate
• Cellobiose and glucose are colorless when dissolved
cellobiose
p-nitrophenyl glucopyranoside
• modified substrate colorimetric detection
Background – cellobiase detection system

## Slide 11: Cellobiase breakdown of p-nitrophenyl glucopyranoside
+
p-nitrophenyl glucopyranoside + H2O glucose + p-nitrophenol
Basic conditions
Clear
Yellow
Background – cellobiase detection system

## Slide 12: How can this enzymatic reaction be easily quantified?
Basic solution (STOP SOLUTION):
- will develop color of any p-nitrophenol present
- will stop the reaction
Qualitative – Visually Compare vs p-nitrophenol Standards
Quantitative- read absorbance at 410 nm using a spectrophotometer or microplate reader.
Background – cellobiase detection system

## Slide 13: Biofuel Enzyme kit Activity 1

## Slide 14: Biofuel Enzyme kit Activity 1
SmartSpec™ Plus
170-2525EDU
Photodiode Array UV-VIS Spectrometer
Measures
  Absorbance , %T
Specifications
  Range: 200-800 nm
  Optical Resolution: ± 2 nm
  Light Source: Xenon Flash Lamp
  Power: 120 VAC, 60 Hz
Standalone Research Grade Instrument

## Slide 15: Biofuel Enzyme Kit Procedure Overview
Activities:
Reaction Rate & Std curve
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Collaborative approach:
  Each student group does activity 1
  Student groups do one activity each from 2-5
  Groups share data
  All groups do activity 6 and share data
Biofuel Enzyme kit Activities

## Slide 16
Standard | Amount of p-nitrophenol (nmol) | Absorbance 410 nm
S1 | 0 | 0
S2 | 12.5 | 0.2
S3 | 25 | 0.4
S4 | 50 | 0.8
S5 | 100 | 1.6
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 17
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 18
Initial reaction rate =
Amount of p-nitrophenol produced (nmol)
Time (min)
Initial reaction rate =
50 nmol - 0 nmol
4 min - 0 min
= 12.5 nmol/min
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 19
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 20
Initial reaction rate =
Amount of p-nitrophenol produced (nmol)
Time (min)
This is the amount of p-nitrophenol produced in 2 minutes
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 21
Amount of p-nitrophenol formed (nmol)
Time (minutes)
1. The initial reaction rate is faster when there is a higher enzyme concentration
High enzyme concentration
Low enzyme concentration
2. Given enough time, the same amount of product will be formed for both the high and low enzyme concentration reactions
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 22
Amount of p-nitrophenol formed (nmol)
Time (minutes)
0.25 mM substrate [Low]
1.5 mM substrate [High]
1. Effect of substrate concentration on the initial rate
2. Final amount of product formed with varying substrate concentrations
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 23
Where can we find things that break down cellulose?
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activities

## Slide 24
Mushrooms – Ecological niche for food
Mycorrhizal –associated with plant roots
  Porcini
  Chanterelle
Saprotrophic – decomposers
  Shiitake
  Morel
  Button
Parasitic – attacks plants
  Honey Mushroom
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Biofuel Enzyme kit Activity 6

## Slide 25
Biofuel Enzyme kit Activities
Using a Micropipette
Plunger
Tip Ejector
Two stops
1st – defines volume
2nd – ejects volume

## Slide 26
Pick a mushroom
Add ~ 0.25g of mushroom to microcentrifuge tube
crush with blunted pipette tip
Add 1,000 µl extraction buffer and continue crushing
Spin down extract in microcentrifuge to separate mushroom particles from liquid fraction or filter and put liquid fraction in new centrifuge tube (~250ul)
Activity 6
Protocol
Biofuel Enzyme kit Activities

## Slide 27
6. Label microplate wells 1-6
7. Add 100ul of Stop solution to wells 1-6
8. Label a 2ml centrifuge tube with your initials and add 1.5ml of substrate
Activity 6
Protocol
Biofuel Enzyme kit Activities

## Slide 28
Activity 6
Protocol
9. Add 125ul of mushroom extract to substrate and start your clock.
10. At the appropriate times remove 100ul from your reaction and add it to the corresponding well of your microplate. Make sure to mix.
11. To make an appropriate blank, add 92ul of extraction buffer to well 6 and 8 ul of mushroom extract.
Biofuel Enzyme kit Activities

## Slide 29
Activity 6
Protocol
Read samples on iMARK Platereader
Reads 400-750nm
Reads 96 samples in under 10 seconds
Onboard printer, but best to connect to sofoware for easy data manipulation
Can do kinetics, plate shaking, etc
Biofuel Enzyme kit Activities

## Slide 30
Standard | Amount of p-nitrophenol (nmol) | Absorbance 410 nm
S1 | 0 | 0
S2 | 12.5 | 0.2
S3 | 25 | 0.4
S4 | 50 | 0.8
S5 | 100 | 1.6
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
Y = mx + b, solve for X
M = slope
b = y-intercept (can use 0 for ease)
Biofuel Enzyme kit Activity 6

## Slide 31
Std curve / Std Reaction Rate
Effect of Temperature
Effect of pH
Effect of Enzyme Concentration
Effect of Substrate Concentration
Bio-prospecting for Celliobiase
X = (y-b)/m
Derive p-nitrophenol concentrations from Abs data
Time | Absorbance 410 nm | Amount of p-nitrophenol (nmol)
#1 – 1 min |  | 
#2 – 2 min |  | 
#3 – 4 min |  | 
#4 – 6 min |  | 
#5 – 8 min |  | 
#6 - Blank |  | 
Biofuel Enzyme kit Activity 6

## Slide 32: Further Studies (not in kit) SDS PAGE Gel of mushroom extracts
shiitake
Beech
Chicken of the Woods
Oyster
King Oyster
Lion’s Mane
Chanterelle
Aspergillus niger
Kaleidoscope marker
Aspergillus niger has 3 cellobiases at 88, 80, 71KD in the literature.
Chanterelle is mycorrhizal, has no activity when assayed and no bands in cellobiase range
Mushroom samples above were dried cubes
Biofuel Enzyme kit – Further Studies

## Slide 33: Cross curriculum approach
Social Studies – debate biofuels
Environmental Science – effects of biofuel production /global warming
Environmental Science – do the bio-prospecting
History – history of oil and other fuels
Engineering – research paper on how biofuels fit with oil infrastructure